## Slide 1: TCP Communication with Cavli Modules AT+QIOPEN & AT+QISEND
Prepared by Allen Reji Samuel
Date: July 2025

## Slide 2: Introduction to Cavli TCP Modules
Cavli manufactures IoT modules supporting LTE, NB-IoT, GSM.
Modules like C10GS, C42QM, and C16QS support TCP/IP.
AT commands are similar to Quectel’s command set.
Used for remote data transfer over TCP/IP.

## Slide 3: AT+QIOPEN – Open a TCP Socket
Syntax: AT+QIOPEN=<link_id>,"<type>","<remote_addr>",<remote_port>,<local_port>,<mode>
Example: AT+QIOPEN=1,"TCP","test.server.com",80,0,0
link_id: Connection ID (0-11)
type: "TCP" or "UDP"
mode: 0 (non-transparent), 1 (transparent)
Returns: +QIOPEN: <link_id>,0 on success

## Slide 4: AT+QISEND – Send TCP Data
Syntax: AT+QISEND=<link_id>,<length>
Waits for > prompt before entering data
End with Ctrl+Z (ASCII 26)
Example: AT+QISEND=1,13 → Hello, World!
Response: SEND OK

## Slide 5: TCP Communication Flow
1. AT+CGDCONT=1,"IP","your_apn"
2. AT+CGATT=1 – Attach to network
3. AT+QIACT=1 – Activate PDP context
4. AT+QIOPEN=1,"TCP","server.com",1234,0,0
5. AT+QISEND=1,<length> – Send data
6. AT+QICLOSE=1 – Close connection

## Slide 6: AT Commands for TCP Maintenance
AT+QICLOSE=1 – Close socket
AT+QISTATE – Check socket state
AT+QIRD – Read incoming data
AT+QIOPEN? – Check status of sockets

## Slide 7: Common Errors & Fixes
+QIOPEN: 1,565 → Connection failed (timeout)
SEND FAIL → Weak signal or socket not open
+CME ERROR: 3 → SIM not ready
Check: AT+CSQ, AT+CPIN?, AT+QIACT?

## Slide 8: IoT Use Case Examples
Sending real-time sensor data to a server
Smart meter reporting and remote control
Vehicle telemetry using TCP/IP sockets
Device-to-cloud communication

## Slide 9: References
Cavli Module AT Command Manual
Quectel TCP/IP AT Commands Guide
Datasheets: C10GS, C16QS, C42QM
Tested on real modem using TeraTerm/minicom